## Slide 1: April 25, 2012 Steve Westenbroek Wisconsin Water Science Center
Meet swb
(Soil-Water-Balance Model)

## Slide 2: swb
what is it?
what does it do?
why would I want to use it?
how can it support my work?

## Slide 3: what is swb?
grid-based
modified Thornthwaite-Mather approach
daily timestep
accounts for:
  snow accumulation / melting
  runon / runoff
  interception
  evapotranspiration
  runoff from frozen ground
http://pubs.usgs.gov/tm/tm6-a31/

## Slide 4: what is a “Thornthwaite-Mather approach”?
Source: Thornthwaite and Mather, 1957

## Slide 5
Source: Thornthwaite and Mather, 1957
“From a comparison of the seasonal march of precipitation with evapotranspiration, the magnitude of other related moisture parameters, the water surplus, water deficit, soil moisture storage, and water runoff may be determined.”
potential recharge,

## Slide 6: seasonal march of P and PE
Modified from: Thornthwaite and Mather, 1955
Precip
potET
actET
Surplus
Deficit
Soil moisture
(-) (+)
soil moisture utilization
soil moisture “recharge”

## Slide 7: application of Thornthwaite and Mather’s method
Modified from: Thornthwaite , 1958

## Slide 8: swb water balance
interception
storage
soil storage
snow
storage
snowmelt
runoff
runoff
rainfall
snowfall
potential recharge
evapotranspiration
[upslope cell]
[downslope cell]

## Slide 9: swb water balance
snow
storage
snowmelt
snowfall
Corps of Engineers
PRMS

## Slide 10: swb water balance
interception
storage
soil storage
snow
storage
snowmelt
runoff
runoff
rainfall
snowfall
potential recharge
evapotranspiration
[upslope cell]
[downslope cell]

## Slide 11: swb water balance
evapotranspiration
Thornthwaite-Mather
Turc
Jensen-Haise
Blaney-Criddle
Hargreaves-Samani

## Slide 12: swb water balance
interception
storage
soil storage
snow
storage
snowmelt
runoff
runoff
rainfall
snowfall
potential recharge
evapotranspiration
[upslope cell]
[downslope cell]

## Slide 13: how much moisture can be pulled from the soil?
Source: Thornthwaite and Mather, 1957
Accumulated Potential Water Loss (APWL)
Maximum Soil Moisture Capacity

## Slide 15: many existing tools for estimating potential recharge

## Slide 16: swb is easy to begin using
Soil hydrologic group
D8 flow direction
Available water
content
Land use / land
cover
Potential recharge
Gridded or tabular
daily precipitation, minimum
and maximum air temperature
swb

## Slide 17: swb designed from the start for groundwater problems
Source: Dripps, 2003

## Slide 18: swb designed to work with PEST
SWB
Observed
SWB
Observed
SWB
Observed
SWB
Observed
January 10, 2000
January 23, 2000
February 25, 2000
March 14, 2000

## Slide 19: Initial SWB-derived recharge
Mean annual recharge for the period 1989-2000
Mean annual recharge for various periods, usually 1970-2000
USGS gage-derived recharge
(Gebert and others, 2007)

## Slide 20: Current version: ported to Fortran 95/2003
  Co-conspirators:
  Wes Dripps
  Randy Hunt
  Vic Kelson
  Ken Bradbury

## Slide 21: swb was designed to be easily modified!

## Slide 22: swb: irrigation demand
Source: Allen, R.G., Pereira, L.S., Raes, D. and Smith, M., 1998, Crop evapotranspiration-Guidelines for computing crop water requirements-FAO Irrigation and drainage paper 56: Rome, Food and Agriculture Organization of the United Nations, accessed May 5, 2011, at http://www.fao.org/docrep/X0490E/x0490e00.htm#Contents.

## Slide 23: swb: irrigation demand
Source: Allen, R.G., Pereira, L.S., Raes, D. and Smith, M., 1998, Crop evapotranspiration-Guidelines for computing crop water requirements-FAO Irrigation and drainage paper 56: Rome, Food and Agriculture Organization of the United Nations, accessed May 5, 2011, at http://www.fao.org/docrep/X0490E/x0490e00.htm#Contents.

## Slide 24: swb: irrigation demand

## Slide 25: Je-ju Island, South Korea

## Slide 26: Je-ju Island, South Korea
Too much ET taken from soil storage (no ET from interception storage)

## Slide 27: swb needs better tools for munging output

## Slide 28: swb needs a better way of obtaining gridded daily climate data!

## Slide 29: swb on the web…

## Slide 30: The future of swb?
Mean annual recharge for the period 1989-2000
All programs evolve until they can send email.
- Richard Letts

## Slide 31
Units: millions of acre-feet per year

## Slide 32
Units: millions of acre-feet per year

## Slide 34: Mean Annual Recharge: 1901-2000
1992 Land Use
“Predevelopment” Land Use
Mean recharge
(excluding open water): 7.34 inches
Mean recharge
(excluding open water): 6.94 inches

## Slide 35: Mean Annual Recharge: 1900-2000
“MEAN RECHARGE”: landuse = 1992 National Land Cover Dataset
“PREDEV MEAN RECHARGE”: landuse = composite vegetative land cover from surveyor’s records – ~1835 - ~1870
“URBAN CN MEAN RECHARGE”: landuse= 1992 NLCD; CN for high-density and low-density urban set to 92 and 86,
regardless of soil type, on theory that urbanized areas have disturbed, compacted soils that little resemble their
underlying soil hydrologic groups. (Lim and others, 2006, “Effects of initial abstraction and urbanization on estimated runoff
using curve number technology”, Journal of the American Water Resources Association, June, 2006.)

## Slide 36: Mean Annual Recharge: 1900-2000

## Slide 37: Land cover as interpreted from survey records ~ 1820’s through 1850’s

## Slide 38: Land cover – National Land Cover Dataset (1992)

## Slide 39: Initial SWB-derived recharge
Mean annual recharge for the period 1989-2000

## Slide 40
1945
1955
1965
1975
Irrigated corn and soybeans shown in purple