## Slide 1: August 6, 2012 Steve Westenbroek Wisconsin Water Science Center
Theory and application of
swb
(Soil-Water-Balance Model)

## Slide 2: contaminated sediments

## Slide 3: dam removals

## Slide 4: building casinos(!)

## Slide 5: shear stress studies

## Slide 6: hydrodynamic modeling

## Slide 7: soil-water-balance model
_d:\SMWData\Source_Code\SWB_TEST_CASES\Coshocton\swb>swb
Soil Water Balance Code version 1.1 -- compiled on: Aug 5 2012 11:48:06
Compiled with: GNU gfortran version 4.6.2
Compilation options:
----------------------------------
STREAM_INTERACTIONS no
GRAPHICS_SUPPORT yes
NETCDF_SUPPORT yes
STRICT_DATE_CHECKING no
THORNTHWAITE_MATHER_TABLE yes
DEBUG_PRINT no
Usage: swb [control file name]

## Slide 8: part 1: introduction and capabilities
what is swb?
what kinds of problems has swb been used for?
what are the positives of swb?
what are the negatives of swb?
how does it compare to other similar tools?

## Slide 9: part 2: under the hood
Thornthwaite-Mather methodology
mechanisms used to simulate components of the water balance

## Slide 10: part 3: simple application example
data sources
data wrangling
  gridded data
  tabular data
other considerations:
  grid cell resolution
  representation of land use and soils

## Slide 11: part 4: tools, tips, and tricks for more advanced applications
gridded precipitation and temperature grids
netCDF(!)
PEST
use of irrigation module
accessing swb output:
  swbstats, R/Python modules
what to do when swb bombs

## Slide 12: part 4.5: future of swb
Doxygen and documentation
GitHub and collaboration
@TODO list
features vs. performance

## Slide 13: what is swb?
grid-based
modified Thornthwaite-Mather approach
daily timestep
accounts for:
  snow accumulation / melting
  runon / runoff
  interception
  evapotranspiration
  runoff from frozen ground
http://pubs.usgs.gov/tm/tm6-a31/

## Slide 15: many existing tools for estimating potential recharge

## Slide 16
 | Basin Charac-teristics | INFIL 3.0 | WetSpa | HELP (v3) | Deep Percolation | Versatile Soil Moisture Budget | SWB
Soil layers |  | Multiple (6) |  | Multiple | Multiple | Multiple | Single
Grid-based | Yes | Yes | Yes | No | Yes | Yes | Yes
Interception |  | NA |  |  | Bucket | NA | Simple bucket (empties daily; doesn’t affect ET)
Infiltration / Runoff |  |  |  |  | Curve number, modified by observed Q | Modified curve number | Curve number
Interflow |  |  | Darcy’s Law / kinematic approx. |  | NA |  | NA
Irrigation demand |  | NA |  | NA | User supplies application rates |  | Calculated by FAO-56 methodology
Soil moisture |  |  | Modified Thornthwaite-Mather |  | Mass balance w Zahner (1967) soil moisture retention fxns |  | Thornthwaite-Mather / FAO-56
Snow sublimation, drifting, etc. |  |  |  |  | Yes | Yes | No
Snow accumulation |  |  |  |  | Anderson (1973) |  | 
Snowmelt |  |  |  |  |  |  | 
Runoff from frozen ground |  |  |  |  | NA |  | CFGI and Curve Number modification
Runoff routing |  | Yes |  | No | No |  | Yes
Potential Evapotranspiration |  | Priestly-Taylor |  |  | Jensen-Haise |  | 
Vegetation modulates AET |  |  |  |  | Yes (crop coefficient) | Yes (crop coefficient) | No; Yes (crop coefficients)

## Slide 17
 | Basin Charac-teristics | INFIL 3.0 | WetSpa | HELP (v3) | Deep Percolation | Versatile Soil Moisture Budget | SWB
Climate data: |  |  |  |  |  |  | 
Interpolated on-the-fly (if gridded)? |  | Yes. Multiple regresssion / IDW |  | NA | Yes. Variety of ways to interpolate climate data. |  | No. Must be pregridded.
Landuse data |  |  |  |  | Dynamic (annual) |  | Dynamic (annual)
Grid-based | Yes | Yes | Yes | No | Yes | No | Yes
Maximum grid dimension |  | 60,005 |  | NA | ? Can likely be recompiled with greater dimensions |  | Limited by available memory (> 100,000)
GIS Data (GRIDS) as input? |  |  |  |  | No | ??? | Yes
NetCDF files as input? |  |  |  |  | No | ??? | Yes
Timescale | Monthly | Daily / hourly |  |  | Daily | Daily | Daily
Other |  |  | ArcView 3.3 extension |  | Several routines are tailored to the Pacific NorthWest |  | 

## Slide 18: swb is easy to begin using
Soil hydrologic group
D8 flow direction
Available water
content
Land use / land
cover
Potential recharge
Gridded or tabular
daily precipitation, minimum
and maximum air temperature
swb

## Slide 19: swb designed from the start for groundwater problems
Source: Dripps, 2003

## Slide 20: swb designed to work with PEST
SWB
Observed
SWB
Observed
SWB
Observed
SWB
Observed
January 10, 2000
January 23, 2000
February 25, 2000
March 14, 2000

## Slide 21: Initial SWB-derived recharge
Mean annual recharge for the period 1989-2000
Mean annual recharge for various periods, usually 1970-2000
USGS gage-derived recharge
(Gebert and others, 2007)

## Slide 22: Current version: ported to Fortran 95/2003
  Co-conspirators:
  Wes Dripps
  Randy Hunt
  Vic Kelson
  Ken Bradbury

## Slide 23: swb was designed to be easily modified!

## Slide 24: Mean Annual Recharge: 1901-2000
1992 Land Use
“Predevelopment” Land Use
Mean recharge
(excluding open water): 7.34 inches
Mean recharge
(excluding open water):
6.94 inches

## Slide 25: swb: irrigation demand

## Slide 26: Je-ju Island, South Korea

## Slide 27: Je-ju Island, South Korea
Too much ET taken from soil storage
(no ET from interception storage)

## Slide 28: swb needs better tools for munging output

## Slide 29: swb needs a better way of obtaining gridded daily climate data!

## Slide 30: swb on the web…

## Slide 31: The future of swb?
Mean annual recharge for the period 1989-2000
All programs evolve until they can send email.
- Richard Letts

## Slide 32
Units: millions of acre-feet per year

## Slide 33
Units: millions of acre-feet per year

## Slide 35: Mean Annual Recharge: 1900-2000
“MEAN RECHARGE”: landuse = 1992 National Land Cover Dataset
“PREDEV MEAN RECHARGE”: landuse = composite vegetative land cover from surveyor’s records – ~1835 - ~1870
“URBAN CN MEAN RECHARGE”: landuse= 1992 NLCD; CN for high-density and low-density urban set to 92 and 86,
regardless of soil type, on theory that urbanized areas have disturbed, compacted soils that little resemble their
underlying soil hydrologic groups. (Lim and others, 2006, “Effects of initial abstraction and urbanization on estimated runoff
using curve number technology”, Journal of the American Water Resources Association, June, 2006.)

## Slide 36: Mean Annual Recharge: 1900-2000

## Slide 37: Land cover as interpreted from survey records ~ 1820’s through 1850’s

## Slide 38: Land cover – National Land Cover Dataset (1992)

## Slide 39: Initial SWB-derived recharge
Mean annual recharge for the period 1989-2000

## Slide 40
1945
1955
1965
1975
Irrigated corn and soybeans shown in purple

## Slide 41: Summary for 8/8/2007 SWB run #2
Alternative INITIAL ABSTRACTION method used (Hawkins, 2002); Ia = 0.05S
Continuous Frozen Ground Index (CFGI) = 83
Hargreaves (1985) PET
Curve numbers dynamically linked to antecedant moisture condition (i.e. as originally coded)
Flattened curve numbers for urban areas (i.e. single curve number for all soil types; reflective of compacted nature of urban soils)
Land use grid eliminates all open water cells save for Lake Michigan AND Lake Winnebago
Overland flow routing in SWB was disabled for all pilot project simulations
Simulation period covered January 1, 1989 through December 31, 2000
Model domain consisted of 316 cells by 410 cells, 5000 ft in length on each side

## Slide 42: Percentiles summary for 8 August 2007 – Run #2

## Slide 43: Percentiles summary for 8 August 2007 – Run #2
LAND USE TYPES
21: low-density residential
41: deciduous forest
81: Pasture / grassland
82: Row crops
91: Forested wetland

## Slide 44: Percentiles summary for 8 August 2007 – Run #2

## Slide 45: Regression summary for 8 August 2007 – Run #2
Source data: SWB run 8 AUG 2007 v2

## Slide 46: Summary of estimated recharge by land use: 8 AUG 2007 – Run #2
Source data: SWB run 8 AUG 2007 v2

## Slide 47: Summary of mean estimated POTENTIAL RECHARGE by land use and soil type
SOIL TYPE
Source data: SWB run 8 AUG 2007 v2

## Slide 48: Summary of AWC times rooting depth by land use and soil type
AWC: Available Water Capacity (inches of water per foot of soil depth)
All things being equal, recharge is roughly α 1 / (AWC times rooting depth)
AWC values applied to Fullerton soil types:
  1) CLAY TILL: 3.4 inches
  2) LOAMY TILL: 2.2 inches
  3) FINE STRATIFIED: 3.0 inches
  4) MEDIUM and COARSE STRATIFIED: 1.4 inches
  5) ORGANIC: 2.0 inches
Source data: SWB run 8 AUG 2007 v2

## Slide 49: Ratio: SWB to Qb (Q90 regression)
Source data: SWB run 8 AUG 2007 v2

## Slide 50: Curve numbers used for 8/8/2007 Run #2

## Slide 51: Root zone depths (ft) by AWC used for 8/8/2007 Run #2
SOIL AVAILABLE
WATER CONTENT
(INCHES PER FOOT)

## Slide 52: Soils layer used for 8 August SWB Run #2

## Slide 53: Land use classification layer used in 8 August 2007 Run #2
Notes: Daniel and Randy: here is a simple way arounf the issue that Daniel and I discussed this morning: convert “OPEN WATER” cells to “WOODY WETLAND”. That is not to say that each of these cells is truly representative of woody wetland, but it will force SWB to calculate a midrange recharge value rather than kicking out zero recharge. Probably not a bad approximation for northern MI and WI.

## Slide 54: Available Water Capacity layer used for 8 August SWB Run #2

## Slide 55: Root depth times AWC for 8 August SWB Run #2

## Slide 56: Precipitation and temperature inputs to the SWB code
Data from 250 NOAA cooperative climate stations pulled for the period 1989-2000
Interpolations made for each day of the simulation period
Thin plate spline interpolations performed on daily minimum and maximum air temperature and precipitation data
Each daily interpolation saved as an ASCII Arc GRID file for use as input to the soil water balance code (> 3650 files)

## Slide 57: Example Soil Moisture Balance Inputs and Outputs - 1994

## Slide 58: Final recharge grid: average of 1991-2000 annual estimates
Multidirectional Lee Filter
Unfiltered
Source data: SWB run 8 AUG 2007 v2

## Slide 59: References
J. S. Lee. Digital image enhancement and noise filtering by use of local statistics.
IEEE Transactions on Pattern Analysis and Machine Intelligence, PAMI-2:165-168, 1980.